## Slide 1: Computer Architecture
Chapter 5: Digital Building Blocks
Largely based on slides by David and Sarah Harris

## Slide 2: Chapter 5 Topics
Introduction
Arithmetic Circuits
Number Systems
Sequential Building Blocks
Memory Arrays
Logic Arrays

## Slide 3: Introduction
Digital building blocks:
  Gates, multiplexers, decoders, registers, arithmetic circuits, counters, memory arrays, logic arrays
Building blocks demonstrate hierarchy, modularity, and regularity:
  Hierarchy of simpler components
  Well-defined interfaces and functions
  Regular structure easily extends to different sizes
Will use these building blocks in Chapter 7 to build microprocessor

## Slide 4: Adders
1-bit Adder
Multibit Adder
Ripple-Carry Adder
Carry-Lookahead Adder
Prefix Adder

## Slide 5: 1-bit Adders

## Slide 6: 1-bit Adders

## Slide 7: 1-bit Adders

## Slide 8: Multibit Adders (CPAs)
Types of carry propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
Carry-lookahead and prefix adders faster for large adders but require more hardware

## Slide 9: Ripple-Carry Adder
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow

## Slide 10: Ripple-Carry Adder Delay
tripple = NtFA
where tFA is the delay of a full adder

## Slide 11: Exercise
What are S and C when the following operations are performed respectively by a 4-bit ripple-carry adder? Assume Cin=0
  1011 + 0010
  0101 + 1100

## Slide 12: Carry-Lookahead Adder
Compute carry out (Cout) for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Column i will generate a carry out if Ai AND Bi are both 1.
  Gi = Ai Bi
    Column i will propagate a carry in to the carry out if Ai OR Bi is 1.
  Pi = Ai + Bi
    The carry out of column i (Ci) is:
  Ci = Ai Bi + (Ai + Bi )Ci-1 = Gi + Pi Ci-1

## Slide 13: Full Adder

## Slide 14: Carry-Lookahead Addition
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate block

## Slide 15: Carry-Lookahead Adder
Example: 4-bit blocks (G3:0 and P3:0) :
  G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 )
  P3:0 = P3P2 P1P0
Generally,
  Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2Gj )
  Pi:j = PiPi-1 Pi-2Pj
  Ci = Gi:j + Pi:j Ci-1

## Slide 16: 32-bit CLA with 4-bit Blocks

## Slide 17: Exercise
0101+1100

## Slide 18: Carry-Lookahead Adder Delay
For N-bit CLA with k-bit blocks:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
  tpg : delay to generate all Pi, Gi
  tpg_block : delay to generate all Pi:j, Gi:j
  tAND_OR : delay from Cin to Cout of final AND/OR gate in k-bit CLA block
tFA
tFA
tFA
tFA
tAND_OR
tpg
tpg_block
tFA
tFA
tFA
tFA
tAND_OR
tpg
tpg_block
tFA
tFA
tFA
tFA
tAND_OR
tpg
tpg_block
tFA
tFA
tFA
tFA
tAND_OR
tpg
tpg_block

## Slide 19: Prefix Adder
Computes carry in (Ci-1) for each column, then computes sum:
Si = (Ai Å Bi) Å Ci
Computes G and P for 1-, 2-, 4-, 8-bit blocks, etc. until all Gi (carry in) known
log2N stages

## Slide 20: Prefix Adder
Generate and propagate signals for a block spanning bits i :j :
  Gi:j = Gi:k + Pi:k Gk-1:j
  Pi:j = Pi:kPk-1:j
In words:
  Generate: block i :j will generate a carry if:
    upper part ( i :k ) generates a carry or
    upper part propagates a carry generated in lower part ( k-1:j )
  Propagate: block i :j will propagate a carry if both the upper and lower parts propagate the carry

## Slide 21: Prefix Adder
Carry in either generated in a column or propagated from a previous column.
Column -1 holds Cin, so
  G-1 = Cin, P-1 = 0
Carry in to column i = carry out of column i-1:
  Ci-1 = Gi-1:-1
Gi-1:-1: generate signal spanning columns i-1 to -1
Sum equation:
  Si = (Ai Å Bi) Å Gi-1:-1
Goal: Quickly compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (called prefixes)

## Slide 22: Prefix Adder Schematic

## Slide 23: Exercise
0101 + 1100

## Slide 24: Prefix Adder Delay
tPA = tpg + log2N(tpg_prefix ) + tXOR
  tpg: delay to produce Pi Gi (AND or OR gate)
  tpg_prefix: delay of black prefix cell (AND-OR gate)

## Slide 25: Adder Delay Comparisons
Compare delay of: 32-bit ripple-carry, carry-lookahead, and prefix adders
CLA has 4-bit blocks
2-input gate delay = 100 ps; full adder delay = 300 ps
tripple = NtFA = 32(300 ps)
= 9.6 ns
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [100 + 600 + (7)200 + 4(300)] ps
= 3.3 ns
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [100 + log232(200) + 100] ps
= 1.2 ns

## Slide 26: Subtracter

## Slide 27: Comparator: Equality

## Slide 28: Comparator: Less Than

## Slide 29: Arithmetic Logic Unit (ALU)
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT

## Slide 30: ALU Design
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT

## Slide 31: Set Less Than (SLT) Example
Configure 32-bit ALU for SLT operation: A = 25 and B = 32
  A < B, so Y should be 32-bit representation of 1 (0x00000001)
  F2:0 = 111
    F2 = 1 (adder acts as subtracter), so 25 - 32 = -7
    -7 has 1 in the most significant bit (S31 = 1)
    F1:0 = 11 multiplexer selects Y = S31 (zero extended) = 0x00000001

## Slide 32: Shifters
1
1
0
1
0
1
1
0
1
1
0
1
0
1
1
0
Shift to the right
1
1
0
1
0
1
1
?
Pad zero to the empty space (logical shift)
Extend the sign bit to the empty space (arithmetic shift)

## Slide 33: Shifters
1
1
0
1
0
1
1
0
0
1
0
1
0
1
1
1
Shift to the left
0
1
0
1
1
0
1
0
Pad zero to the empty space (logical/arithmetic shift)

## Slide 34: Rotator
1
1
0
1
0
1
1
0
1
1
0
1
0
1
1
0
Rotate to the right
1
1
0
1
0
1
1
0

## Slide 35: Shifters
Logical shifter: shifts value to left or right and fills empty spaces with 0’s
  Ex: 11001 >> 2 =
  Ex: 11001 << 2 =
Arithmetic shifter: same as logical shifter, but on right shift, fills empty spaces with the old most significant bit (msb).
  Ex: 11001 >>> 2 =
  Ex: 11001 <<< 2 =
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 =
  Ex: 11001 ROL 2 =

## Slide 36: Shifters
Logical shifter:
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter:
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator:
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111

## Slide 37: Shifter Design

## Slide 38: Barrel Shifter

## Slide 39: Shifters as Multipliers, Dividers
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)

## Slide 40: Multipliers
Partial products formed by multiplying a single digit of the multiplier with multiplicand
Shifted partial products summed to form result

## Slide 41: 4 x 4 Multiplier

## Slide 42: 4 x 4 Divider
A/B = QB + R
Algorithm:
R’ = 0
for i = N-1 to 0
R = {R’ << 1. Ai}
D = R - B
if D < 0, Qi=0, R’=R
else Qi=1, R’=D
R = R’
B3
B2
B1
B0
B3
B2
B1
B0
B3
B2
B1
B0
B3
B2
B1
B0
A3
A2
A1
A0
Q3
Q2
Q1
Q0
R0
R1
R2
R3
0
0
0
1
1
1
1

## Slide 43: Exercise
Compute 1010 / 11
0011
11 1010
0
10
00
101
11
100
11
1
i=3)
R = (R’<<1). A3 = 1
D = R-B = 1 – 11 < 0
Q3 = 0, R’ = R = 1
i=2)
R = (R’<<1). A2 = 10
D = R-B = 10 – 11 < 0
Q2 = 0, R’ = R = 10
i=1)
R = (R’<<1). A1 = 101
D = R-B = 101 – 11 > 0
Q1 = 1, R’ = D = 10
i=0)
R = (R’<<1). A0 = 100
D = R-B = 100 – 11 > 0
Q0 = 1, R’ = D = 1
A/B = QB + R
Algorithm:
R’ = 0
for i = N-1 to 0
R = {R’ << 1. Ai}
D = R - B
if D < 0, Qi=0, R’=R
else Qi=1, R’=D
R = R’

## Slide 44: Counters
Increments on each clock edge
Used to cycle through numbers. For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
Example uses:
  Digital clock displays
  Program counter: keeps track of current instruction executing

## Slide 45: Shift Registers
Shift a new bit in on each clock edge
Shift a bit out on each clock edge
Serial-to-parallel converter: converts serial input (Sin) to parallel output (Q0:N-1)
Implementation:
Symbol:

## Slide 46: Shift Register with Parallel Load
When Load = 1, acts as a normal N-bit register
When Load = 0, acts as a shift register
Now can act as a serial-to-parallel converter (Sin to Q0:N-1) or a parallel-to-serial converter (D0:N-1 to Sout)

## Slide 47: Number Systems
Numbers we can represent using binary representations
  Positive numbers
    Unsigned binary
  Negative numbers
    Two’s complement
    Sign/magnitude numbers
What about fractions?

## Slide 48: Numbers with Fractions
Two common notations:
  Fixed-point: binary point fixed
  Floating-point: binary point floats to the right of the most significant 1

## Slide 49: Fixed-Point Numbers
6.75 using 4 integer bits and 4 fraction bits:
  Binary point is implied
  The number of integer and fraction bits must be agreed upon beforehand

## Slide 50: Fixed-Point Number Example
Represent 7.510 using 4 integer bits and 4 fraction bits.
  01111000

## Slide 51: Signed Fixed-Point Numbers
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  11111000
  Two’s complement:
  1. +7.5: 01111000
  2. Invert bits: 10000111
  3. Add 1 to lsb: + 1
  10001000

## Slide 52: Floating-Point Numbers
Binary point floats to the right of the most significant 1
Similar to decimal scientific notation
For example, write 27310 in scientific notation:
  273 = 2.73 × 102
In general, a number is written in scientific notation as:
± M × BE
  M = mantissa
  B = base
  E = exponent
  In the example, M = 2.73, B = 10, and E = 2

## Slide 53: Floating-Point Numbers
Example: represent the value 22810 using a 32-bit floating point representation
  We show three versions –final version is called the IEEE 754 floating-point standard

## Slide 54: Floating-Point Representation 1
Convert decimal to binary (don’t reverse steps 1 & 2!):
  22810 = 111001002
Write the number in “binary scientific notation”:
  111001002 = 1.110012 × 27
Fill in each field of the 32-bit floating point number:
  The sign bit is positive (0)
  The 8 exponent bits represent the value 7
  The remaining 23 bits are the mantissa

## Slide 55: Floating-Point Representation 2
First bit of the mantissa is always 1:
  22810 = 111001002 = 1.11001 × 27
So, no need to store it: implicit leading 1
Store just fraction bits in 23-bit field

## Slide 56: Floating-Point Representation 3
Biased exponent: bias = 127 (011111112)
  Biased exponent = bias + exponent
  Exponent of 7 is stored as:
  127 + 7 = 134 = 0x100001102
The IEEE 754 32-bit floating-point representation of 22810
in hexadecimal: 0x43640000

## Slide 57: Floating-Point Example
Write -58.2510 in floating point (IEEE 754)
Convert decimal to binary:
  58.2510 = 111010.012
Write in binary scientific notation:
1.1101001 × 25
Fill in fields:
  Sign bit: 1 (negative)
  8 exponent bits: (127 + 5) = 132 = 100001002
  23 fraction bits: 110 1001 0000 0000 0000 0000
in hexadecimal: 0xC2690000

## Slide 58: Floating-Point: Special Cases
Number | Sign | Exponent | Fraction
0 | X | 00000000 | 00000000000000000000000
∞ | 0 | 11111111 | 00000000000000000000000
- ∞ | 1 | 11111111 | 00000000000000000000000
NaN | X | 11111111 | non-zero

## Slide 59: Floating-Point Precision
Single-Precision:
  32-bit
  1 sign bit, 8 exponent bits, 23 fraction bits
  bias = 127
Double-Precision:
  64-bit
  1 sign bit, 11 exponent bits, 52 fraction bits
  bias = 1023

## Slide 60: Floating-Point: Rounding
Overflow: number too large to be represented
Underflow: number too small to be represented
Rounding modes:
  Down
  Up
  Toward zero
  To nearest
Example: round 1.100101 (1.578125) to only 3 fraction bits
  Down: 1.100
  Up: 1.101
  Toward zero: 1.100
  To nearest: 1.101 (1.625 is closer to 1.578125 than 1.5 is)

## Slide 61: Floating-Point Addition
Extract exponent and fraction bits
Prepend leading 1 to form mantissa
Compare exponents
Shift smaller mantissa if necessary
Add mantissas
Normalize mantissa and adjust exponent if necessary
Round result
Assemble exponent and fraction back into floating-point format

## Slide 62: Floating-Point Addition Example
Add the following floating-point numbers:
0x3FC00000
0x40500000

## Slide 63: Floating-Point Addition Example
1. Extract exponent and fraction bits
For first number (N1): S = 0, E = 127, F = .1
For second number (N2): S = 0, E = 128, F = .101
2. Prepend leading 1 to form mantissa
N1: 1.1
N2: 1.101

## Slide 64: Floating-Point Addition Example
3. Compare exponents
128 – 127 = 1, so shift N1 right by 1 bit
4. Shift smaller mantissa if necessary
shift N1’s mantissa: 1.1 >> 1 = 0.11 (× 21)
5. Add mantissas
0.11 × 21
+ 1.101 × 21
10.011 × 21

## Slide 65: Floating-Point Addition Example
6. Normalize mantissa and adjust exponent if necessary
10.011 × 21 = 1.0011 × 22
7. Round result
No need (fits in 23 bits)
8. Assemble exponent and fraction back into floating-point format
S = 0, E = 2 + 127 = 129 = 100000012, F = 001100..
in hexadecimal: 0x40980000

## Slide 66: Memory Arrays
Efficiently store large amounts of data
3 common types:
  Dynamic random access memory (DRAM)
  Static random access memory (SRAM)
  Read only memory (ROM)
M-bit data value read/ written at each unique N-bit address

## Slide 67: Memory Arrays
2-dimensional array of bit cells
Each bit cell stores one bit
N address bits and M data bits:
  2N rows and M columns
  Depth: number of rows (number of words)
  Width: number of columns (size of word)
  Array size: depth × width = 2N × M

## Slide 68: Memory Array Example
22 × 3-bit array
Number of words: 4
Word size: 3-bits
For example, the 3-bit word stored at address 10 is 100

## Slide 69: Memory Array
Wordline:
  like an enable
  single row in memory array read/written
  corresponds to unique address
  only one wordline HIGH at once

## Slide 70: Memory Array Bit Cells
0
1
Z
Z

## Slide 71: Types of Memory
Random access memory (RAM): volatile
Read only memory (ROM): nonvolatile

## Slide 72: RAM: Random Access Memory
Volatile: loses its data when power off
Read and written quickly
Main memory in your computer is RAM (DRAM)
Historically called random access memory because any data word accessed as easily as any other (in contrast to sequential access memories such as a tape recorder)

## Slide 73: ROM: Read Only Memory
Nonvolatile: retains data when power off
Read quickly, but writing is impossible or slow
Flash memory in cameras, thumb drives, and digital cameras are all ROMs (nonvolatile memories)
  Historically called read only memory because ROMs were written at manufacturing time or by burning fuses. Once ROM was configured, it could not be written again. This is no longer the case for Flash memory and other types of ROMs.

## Slide 74: Types of RAM
DRAM (Dynamic random access memory)
SRAM (Static random access memory)
Differ in how they store data:
  DRAM uses a capacitor
  SRAM uses cross-coupled inverters

## Slide 75: Robert Dennard, 1932 -
Invented DRAM in 1966 at IBM
Others were skeptical that the idea would work
By the mid-1970’s DRAM in virtually all computers

## Slide 76: DRAM
Data bits stored on capacitor
Dynamic because the value needs to be refreshed (rewritten) periodically and after read:
  Charge leakage from the capacitor degrades the value
  Reading destroys the stored value

## Slide 77: DRAM

## Slide 78: SRAM

## Slide 79: Memory Arrays Review
DRAM bit cell:
SRAM bit cell:

## Slide 80: DRAM vs SRAM
 | DRAM | SRAM
Speed | Slower | Faster
Size | Smaller | Bigger
Cost | Less expensive | More expensive
Access | Harder | Easier
Construction | Simple | Difficult
Power consumption | More | Less

## Slide 81: ROM: Dot Notation

## Slide 82: ROM Storage

## Slide 83: ROM Logic
Data2 = A1 Å A0
Data1 = A1 + A0
Data0 = A1A0

## Slide 84: Example: Logic with ROMs
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B

## Slide 85: Example: Logic with ROMs
Implement the following logic functions using a 22 × 3-bit ROM:
  X = AB
  Y = A + B
  Z = A B

## Slide 86: Logic with Any Memory Array
Data2 = A1 Å A0, Data1 = A1 + A0, Data0 = A1A0

## Slide 87: Logic with Memory Arrays
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B

## Slide 88: Logic with Memory Arrays
Implement the following logic functions using a 22 × 3-bit memory array:
  X = AB
  Y = A + B
  Z = A B

## Slide 89: Logic with Memory Arrays
Called lookup tables (LUTs): look up output at each input combination (address)

## Slide 90: Multi-ported Memories
Port: address/data pair
3-ported memory
  2 read ports (A1/RD1, A2/RD2)
  1 write port (A3/WD3, WE3 enables writing)
Register file: small multi-ported memory

## Slide 91: Logic Arrays
PLAs (Programmable logic arrays)
  AND array followed by OR array
  Combinational logic only
  Fixed internal connections
FPGAs (Field programmable gate arrays)
  Array of Logic Elements (LEs)
  Combinational and sequential logic
  Programmable internal connections

## Slide 92: PLAs
X = ABC + ABC
Y = AB

## Slide 93: PLAs: Dot Notation

## Slide 94: Exercise
Implement the following logic with ROM and PLA, respectively. Represent your implementation with the DOT notation.
  X = ABC + AB + BC
  Y = ABC + AB
  Z = AB + BC

## Slide 95: FPGA: Field Programmable Gate Array
Composed of:
  LEs (Logic elements): perform logic
  IOEs (Input/output elements): interface with outside world
  Programmable interconnection: connect LEs and IOEs
  Some FPGAs include other building blocks such as multipliers and RAMs

## Slide 96: General FPGA Layout

## Slide 97: LE: Logic Element
Composed of:
  LUTs (lookup tables): perform combinational logic
  Flip-flops: perform sequential logic
  Multiplexers: connect LUTs and flip-flops

## Slide 98: Altera Cyclone IV LE

## Slide 99: Altera Cyclone IV LE
The Spartan CLB has:
  1 four-input LUT
  1 registered output
  1 combinational output

## Slide 100: LE Configuration Example
Show how to configure a Cyclone IV LE to perform the following functions:
  X = ABC + ABC
  Y = AB

## Slide 101: LE Configuration Example
Show how to configure a Cyclone IV LE to perform the following functions:
  X = ABC + ABC
  Y = AB

## Slide 102: FPGA Design Flow
Using a CAD tool (such as Altera’s Quartus II)
  Enter the design using schematic entry or an HDL
  Simulate the design
  Synthesize design and map it onto FPGA
  Download the configuration onto the FPGA
  Test the design